- Select the correct answer for the following questions. Refer to the “Examination Book of Where are the definitions associated with welding as per AWS D1.1 to be found ? (在AWS D1.1什麼章節中可以找到與焊接有關的定義？)

  - ANSI/AWS A2.4

  - ANSI/AWS A3.0

  - Annex B (附錄B)

  - b and c above (上述的b和c)

  - All of the above (上述所有的)

  - Safety precautions to be observed during welding to AWS D1.1 are found in (有關在焊接過程中的安全警示在AWS D1.1的哪一章節中？)

- Annex J (附錄J)

- ANSI Z49.1

- Annex K (附錄K)

- a and b above (上述的a和b)

- All of the above (上述所有的)

  - What does the nonstandard term “downhand” mean ? (非標準術語“平焊”表示什麼意思？)

- Welding vertically downward (垂直的從上往下焊)

- Welding in the flat position (在平面位置焊)

- The pause during electrode changes (在換焊條時的停頓)

- The pause of welding during deslagging (在清除焊渣時的焊接停頓)

- None of the above (無上述任何一個)

  - In what year was the first bridge welding specification published by the AWS ? (AWS在哪一年出版了第一本橋樑焊接技術規範？)

- 1928

- 1934

- 1936

- 1972

- 1988

  - Which of the following steels are intended to be used in work convered by D1.1 ? (下列哪種鋼可以在D1.1控制的工作中使用？)

- All alloy steels with a yield strength of 97,000 psi or less (屈服強度等於或小於97,000psi 的所有合金)

- Low carbon steels, 5/32in. thick (5/32in厚的低碳鋼)

- Low alloy steel with a yield strength of 970 Mpa (屈服強度為970Mpa的低合金鋼)

- Low carbon stainless steels (低碳不銹鋼)

- None of the above (無上述任何一個)

  - In contract documents, welding symbols without dimensions to indicate groove weld details, are (在合同文件中，指明坡口焊縫細節的沒有尺寸的焊接符號是：)

- Mandatory (強制的)

- Recommended (推薦的)

- Not recommended (不推薦)

- Only to be used when reinforcement is required (只有當有加強要求是使用)

- Only required when joint will be cyclically loaded (只有當接頭周期載荷時要求)

  - Fillet welds on the opposite side of a common plane of contact are required to be (在一接觸的共同平板相反一側的角焊縫要求要：)

- Continuous all around (連續全焊)

- Interrupted at the ends of members (在焊件的端部中斷)

- Interrupted at common corners (在共同角處中斷)

- Boxed (returned) at common corners (在共同角處分隔)

- None of the above (無上述任何一個)

  - What is the maximum size of the fillet welds of a lap joint of member 3/8in. thick ? (焊件厚度為3/8in的搭接接頭的角焊縫的最大尺寸是多少？)

- 3/16 in

- 1/4 in

- 5/16 in

- 3/8 in

- Any size at designer’s option except if cyclically loaded (除了如果是循環載荷，設計者可以 選任何尺寸)

  - How are transitions in thickness of a groove joint to be made ? (坡口接頭的過渡厚度是：)

- Chamfering the thicker member after welding (在焊接後對較厚件進行倒角)

- By chamfering the thicker member before welding on one side only (在焊接前僅對較厚件的一邊進行倒角)

- By chamfering the thicker member before welding on both sides only (在焊接前僅對較厚件的二邊進行倒角)

- By sloping the weld surface(s) (把焊縫表面加工成斜面過渡)

- All of the above (上述所有的)

  - What is the maximum allowable stress for CJP groove weld metal splicing two ASTM A-36 steel non-redundant members of equal thickness and width, subject to loading of 2×106 life time stress reversals, assuming the weld reinforcement remains and all such joints are to be radiographed ? (對於連續兩個同樣厚度和寬度的ASTM A-36鋼的非超靜定焊接件，假定保持焊縫加強高並所有如此接頭都要進行射線探傷，在承受2×106連續應力交變載荷下完全熔透坡口焊縫金屬的最大允許應力是多少？)

- 7500 psi

- 10,000 psi

- 13,500 psi

- 16,000 psi

- 18,000 psi

  - What is the minimum tensile strength of steel conforming to ASTM A572, grade 65 ? (符合ASTM A572,65級鋼的最小拉伸強度？)

- 60,000 psi

- 65,000 psi

- 70,000 psi

- 75,000 psi

- 80,000 psi

  - What is the required minimum preheat and interpass temperature for 1 in. thick API 5L grade B steel welded with flux cored arc welding ? (對於用藥芯電弧焊接厚度為1in的API 5L, B級鋼的最小預熱及層間溫度是多少？)

- 150℉

- 100℉

- 50℉

- None (無)

- None except if ambient temperature is ≦ 50℉ (無，除非如果大氣溫度小於等於50℉)

  - May a groove preparation detailed for SMAW be used unchanged for FACW prequalified WPSs (是否用於SMAW坡口詳細準備可以用於FCAW免除評定的WPS而不作任何改變？)

- Yes (可以)

- No (不可以)

- Only if FCAW is used in DCEP mode (只有當藥芯焊絲氣體保護焊為直流反接時)

- Only when welding group I or group II steels are being welded (只有第I和II組別的鋼材焊  接時)

- Only at designers option except if joints are statically loaded (設計人員選擇，除非接頭是靜載)

  - What is the range of groove angles for joint designation BC-P8, as fit up ? (BC-P8焊接接頭組裝時的坡口角度範圍是？)

- 45° to 55°

- 40° to 55°

- 35° to 50°

- 30° to 45°

- 25° to 40°

  - What is the maximum depth of bevel S2 for joint designation B-U3c-S when welding 3-12 in. plate ? (3-1/2英寸厚的板材B-U3c-S形式的接頭坡口深度S2最大是多少？)

- 1-1/4 in.

- 1-1/8 in.

- 1 in.

- 7/8 in.

- 3/4 in.

4.1 Plug and slot tests welded in the horizontal position qualify a WPS in what position(s) ? (橫焊位置的塞焊和槽焊評定能覆蓋什麼位置？)

- All (所有的位置)

- Flat and horizontal (平焊和橫焊位置)

- All except overhead (除了仰焊以外的其他位置)

- Horizontal (橫焊)

- None of the above (以上都不對)

4.2 A groove weld qualification on 1/2 in. plate qualifies a procedure for what range of thicknesses ? (在1/2英寸板材上進行的坡口焊接工藝評定覆蓋的板材厚度範圍？)

- 0 to 1 in.

- 0 to 3/4 in.

- 1/8 in. to 1 in.

- 1/8 in. to 3/4 in.

- None of the above (以上都不對)

4.3 What diameters of electrodes are qualified by a procedure test using a 5/64 in. FCAW electrode ? (用5/64英寸藥芯焊絲進行的工藝評定可以覆蓋的焊絲直徑是多少？)

- All diameters (所有直徑的焊絲)

- 5/64 in. only (只有5/64英寸直徑的焊絲)

- 5/64 in. and smaller (5/64英寸直徑及以下的焊絲)

- 5/64 in. and larger (5/64英寸直徑及以上的焊絲)

- none of the above (以上答案都不對)

4.4 May a qualified WPS for a CJP groove weld be used to weld PJP grooves ? (某坡口焊縫完全熔透的工藝評定可以用於部分熔透的坡口焊接嗎？)

- Yes (可以)

- No (不可以)

- Only when used for T-groove joints with a superimposed fillet weld (只有用於T型接頭坡口焊縫的多層角焊縫)

- Only if designated weld size is demonstrated by three Macro sections (只有達到指定尺寸的焊縫經過三個宏觀浸蝕試驗驗証)

- Only if designated weld size is checked by on-job macro sections (只有達到指定尺寸的焊縫經過現場宏觀浸蝕試驗驗証)

4.5 The minimum length of a T-joint weld test coupon for welder performance qualification is     (用於評定焊工的T型接頭角焊縫試樣的最小尺寸是多少？)

- 6in.

- 7in.

- ≧6in.

- ≧15in.

- 8 in. minimum (最小8英寸)

5.1 How many times may low hydrogen electrodes be rebaked ? (低氫焊條最多可以重新烘乾幾次？)

- Once (一次)

- Twice (兩次)

- Not limited (沒有限制)

- Not limited , except if coating is damaged (除非藥皮被破壞了)

- Not specified (沒有要求)

5.2 What grade or grades of steel should be used for spacers ? (什麼級別的鋼材可以用做嵌條？)

- Any approved (Table 3.1 or Annex M) base metal (所有在表3.1或附錄M被認可的母材)

- Only steels of the 60 ksi class (只有60ksi級別的鋼材)

- Any approved steel matching the weld metal (任何被認可的與母材匹配的鋼材)

- The same as the base metal (與母材相同的鋼材)

- Any grade of steel, as the spacer will be gouged out during welding (任何級別的鋼材。因為 嵌條在清根時會被刨掉)

5.3 What is the allowable deviation from straightness for a 40 foot long primary truss member ?   (對40英寸長的主珩架構件允許的直線度偏差是多少？)

- 1/2 in.

- 7/16 in.

- 3/8 in.

- 5/16 in.

- 1/4 in.

5.4 What is the allowable variation between the center lines of the web and flange of a 30 feet long built-up I-bean ? (30英寸長的組裝工字梁的腹板中心線和翼板中心線間的允許變化值是多少？)

- 1/2 in.

- 7/16 in.

- 3/8 in.

- 5/16 in.

- 1/4 in.

5.5 What is allowable misalignment between members of a butt joint, under any circumstances ?   (在任何情況下，對接焊縫的錯邊允許多少？)

- No misalignment permitted (不允許錯邊)

- 1/8 in.

- 10% of the thickness of the thinner member (較薄件厚度的10%)

- 10% of the thickness of the thicker member (較薄件厚度的10%)

- 3/16 in.

6.1 Who is responsible to ensure that welding equipment conforms to the provisions of 5.11 ? (誰負責保証焊接設備符合5.11條的規定)

- The contractor (承包商)

- The engineer (工程師)

- The welder (焊工)

- The welding inspector (焊接檢驗員)

- Not specified (沒有規定)

6.2 What maximum depth of undercut is permitted in transverse splices of primary members ? (在主要構件中，橫向接縫的咬邊最大允許多深？)

- 0.01 in.

- 1/32 in.

- 1/16 in.

- None permitted (不允許)

- Not specified (沒有要求)

6.3 Except for stiffener-to web joints, the maximum diameter of piping porosity in fillet welds is   (除了腹板加強筋的接頭，角焊縫的管狀氣孔直徑最大允許多少？)

- 1/32 in.

- 1/16 in.

- 3/32 in.

- 1/8 in.

- None of the above (以上答案都不對)

6.4 For a groove welded tension member in 3/4 in. plate, what is the maximum size of fusion discontinuity permitted in a statically loaded member ? (對於3/4英寸板材的受拉構件坡口焊縫，在承受靜載荷時，熔合性缺陷允許的最大尺寸是多少？)

- 1/2 in.

- 7/16 in.

- 3/8 in.

- 5/16 in.

- 1/4 in.

6.5 For the joint in Question 6.4, what designation hole type IQI should be used ? (對於問題6.4中的接頭，應使用什麼標號的孔型像質計？)

- 10

- 12

- 15

- 17

- 20

6.6 In what circumstances, if any, can a CWI whose certification has-expired, accept D1.1 work ? (在什麼情況下一個証書已經過期的CWI可以接受按照D1.1做的工作？)

- Not permitted due to expiry of certification (不允許，因為証書已過期)

- Requires engineer approval (需要工程師批準)

- Permitted with a current visual acuity test (需要視覺靈敏度測試)

- Permitted with current visual acuity test and engineer approval (需要視覺靈敏度測試和工程師批準)

- May only work as a CAWI (只能作為助理焊接檢驗員工作)

6.7 What is the essential wire diameter (of wire type IQI) for the joint in Question 6.4 ? (在問題6.4中的接頭應用的線型像質計在底片上應顯示的鋼絲直徑是多少？)

- 0.010 in.

- 0.013 in.

- 0.016 in.

- 0.020 in.

- 0.025 in.

7.1 What action is required if a crack 1/4 in. long is observed in a standard 5/8 in. stud head ? (如果5/8英寸的螺柱頭部發現一條1/4英寸長的裂紋，則採取什麼行動：)

- No action, use as is (照常使用)

- Repair crack and use (修復裂紋後使用)

- Do not use , replace stud (不能使用，替換螺柱)

- Suitable only for concrete encased studs (只能用做水泥包住的螺柱)

- Notify stud manufacturer (通知螺柱製造商)

7.2 Through what angle are the daily start up test studs to be bent, assuming 360° flash ? (若飛邊為360°，在每天或每班開始生產時進行的螺柱彎曲試驗彎曲角度是多少？)

- Bend test not requested with 360° flash (飛邊為360°時不要求彎曲試驗)

- 30°

- 15°

- 10°

- ±10°

8.1 Which of the following is not a recommended method of cyclic loading improvement ? (下列哪個方法在周期載荷結構的補強和修理時不推薦使用？)

- Toe grinding with a carbide burr or pencil grinder (用筆狀磨頭或砂輪打磨焊趾)

- Toe grinding plus hammer peening (打磨焊趾外加錘擊)

- Toe grinding plus shot peening of the weld toes (打磨焊趾外加焊趾表面噴丸)

- Reshaping of weld toes by TIG welding (TIG修整)

- Hammer peening of weld toes (錘擊焊趾)